Gloves Grasp outside of glove with opposite gloved hand; peel off Hold removed glove in gloved hand Slide fingers of ungloved hand under remaining glove at wrist Peel glove off over first glove Discard gloves in waste container

Gown Unfasten ties Pull away from neck and shoulders, touching inside of gown only Turn gown inside out Fold or roll into a bundle and discard

Goggles or Face Shield To remove, handle by head band or ear pieces Place in designated receptacle for reprocessing or in waste container

Mask or Respirator Grasp bottom, then top ties or elastics and remove Discard in waste container

# Text boxes

SEQUENCE FOR REMOVING PERSONAL PROTECTIVE EQUIPMENT (PPE)